## Slide 1
Homework 1 (Due: March 26th)
(1) Design a Mini-max highpass FIR filter such that (40 scores)
Filter length = 19,  Sampling frequency fs = 8000Hz,  Stop Band 0~2000Hz
Transition band: 2000~2400 Hz,
 Weighting function: W(F) = 1 for passband, W(F) = 0.6 for stop band .  Set  = 0.0001 in Step 5.
0 Hz
2000 Hz
2200 Hz
2400 Hz
Show (a) the frequency response, (b) the impulse response h[n], and (c) the maximal error for each iteration.
※ The Matlab or Python code should be handed out by NTUCool, too.

## Slide 2
(3) Discuss how to implement y[n] = x[n] * h[n] efficiently where h[n] = (0.7n+ (0.6)n+1)u[n], u[n]: unit step function
(10 scores)
(2) (a) How do we convert convolution into an addition operation?
(b) What are two main advantages of the FT in engineering?
(c) From the view point of implementation, what are the disadvantages of the discrete Fourier transform? (15 scores)
(4) Why (a) the step invariance method and (b) the bilinear transform can reduce or avoid the aliasing effect in IIR filter design? (10 scores)
(5) Design the 7-point FIR filter in the MSE sense where the ideal filter is Hd(F) = 1 for |F| < 0.25,
Hd(F) = 0 for 0.25 < |F| < 0.5 (10 scores)
(Cont.)

## Slide 3
(Extra): Answer the questions according to your student ID number. (ended with 0, 1, 2, 3, 5, 6, 7, 8)
(6) (a) Write two reasons why the transition band plays a critical role in Minimax filter design.
(b) Estimate the pass and stop band ripples if filter length = 21, Δt = 0.0002, and the transition band is 1950~2050 Hz.
(c) Estimate the pass and stop band ripples if filter length = 31, Δt = 0.0001, and the transition band is 1750~ 2250 Hz.
In (b)(c), suppose that pass and stop band ripples are equal. (15 scores)